## Slide 1: Parallelising the CPU kernels
mensurflow: add, sub, mul, div and dot with OpenMP
thread 0
thread 1
thread 2
thread 3
One contiguous block of the array per thread
Notes: Overview of how the CPU kernels run in parallel: the helper in parallel.hpp, the block split, the reduction, and the measured results. The four thread colours used here repeat on every slide.

## Slide 2: Where the parallel code sits
add(a, b)
mensurflow, public API
Validate, broadcast
src/ops/elementwise.cpp
dispatch(Add)
src/core/dispatcher.cpp
add_f32
src/backends/cpu/elementwise.cpp
parallel_for
src/backends/cpu/parallel.hpp
Elementwise ops
add, sub, mul and div share one loop and call parallel_for.
Dot product
dot sums per-thread partial results with parallel_sum.
GPU backends
No OpenMP there: cuBLAS, rocBLAS and MPSGraph parallelise on their own.
Notes: The public call goes through validation and the dispatcher to a CPU kernel. Only the kernel layer touches OpenMP, and only through parallel_for / parallel_sum in parallel.hpp.

## Slide 3: Splitting the array
Every thread gets one contiguous block. Block size is rounded up to a multiple of 16 floats.
n = 100, 4 threads: chunk = 25, rounded up to 32
T0
[0, 32)
T1
[32, 64)
T2
[64, 96)
T3
[96, 100)
n = 20, 4 threads: chunk = 5, rounded up to 16
T0
[0, 16)
T1
[16, 20)
T2: no work
T3: no work
A thread whose block starts past the end (begin >= end) simply skips the work.
Notes: With n = 100 and 4 threads the raw chunk is 25, rounded up to 32, so the last thread only gets 4 elements. With n = 20 two threads get nothing, which is fine: they skip.

## Slide 4: Computing each block
inline void block_range(std::int64_t n, std::int64_t threads, std::int64_t id,
std::int64_t& begin, std::int64_t& end) {
const std::int64_t chunk = ((n + threads - 1) / threads + 15) / 16 * 16;
begin = std::min(id * chunk, n);
end = std::min(begin + chunk, n);
}
src/backends/cpu/parallel.hpp
1
Chunk size
ceil(n / threads), so every element is covered.
2
Round up to 16
16 floats = 64 bytes = one cache line.
3
Clamp with min
The last thread gets a short block, or none.
Notes: This is the real block_range from parallel.hpp. Thread id of threads gets [begin, end). The rounding to 16 floats keeps block edges on 64-byte cache lines.

## Slide 5: Why blocks end on cache lines
Split at 16 (what we do)
cache line 0
cache line 1
✓
Each cache line has one writer
Split at 12 (naive)
cache line 0
cache line 1
!
Line 0 is written by both threads: the cores keep invalidating each other's copy (false sharing)
Each square is one float (4 bytes); 16 floats make one 64-byte cache line.
Notes: If two threads write different floats that live in the same 64-byte cache line, the line bounces between their cores. Rounding block sizes to 16 floats makes every block start on a line boundary.

## Slide 6: Running it: parallel_for
if (n > grain && omp_get_max_threads() > 1) {
#pragma omp parallel
{
block_range(n, omp_get_num_threads(),
omp_get_thread_num(), b, e);
if (b < e) body(b, e);
}
return;
}
body(0, n); // small input: run serially
parallel_for(n, [=](auto lo, auto hi) {
for (auto i = lo; i < hi; ++i)
out[i] = op(a[i], b[i]);
}); // the add / sub / mul / div kernel
simplified excerpts
1
Serial fallback
n of 32,768 or fewer, or one thread: run body(0, n) directly.
2
One region
Every thread computes its own range. No locks needed.
3
No pragmas in kernels
add, sub, mul and div differ only in op.
Notes: Simplified excerpt of parallel_for: begin/end are shortened to b/e. The kernel supplies only the inner loop; the pragma lives in one place.

## Slide 7: Reductions without races
Each thread sums its own block
T0
p0
T1
p1
T2
p2
T3
p3
p0 + p1 + p2 + p3
Partials are added in thread order, so a given thread count always gives the same answer.
// parallel_sum, simplified
vector<double> partial(nthreads);
#pragma omp parallel
{
block_range(n, nthreads, id, b, e);
if (b < e) partial[id] = body(b, e);
}
double total = 0;
for (double p : partial) total += p;
// dot: what body(b, e) does
double sum = 0.0;
for (auto i = b; i < e; ++i)
sum += double(x[i]) * double(y[i]);
return sum; // double, not float
Notes: One shared sum would be a data race. Instead each thread returns a partial; the main thread adds them. dot accumulates in double so the result stays close to the exact sum.

## Slide 8: Why small inputs get slower
Large input: 10 million elements
1 thread
thread 0
thread 1
thread 2
thread 3
Best case: four threads finish in about a quarter of the time. Memory-bound ops gain less (next slide).
Small input: 100 thousand elements
1 thread
thread 0
thread 1
thread 2
thread 3
Waking the threads costs more than the work saves.
waking the threads (overhead)
work (colour = thread)
Illustrative, not to scale
Notes: This is why parallel_for has a cutoff: below it the kernel runs serially. Our current cutoff (32,768 elements) is too low: at 100,000 elements the threaded version was slower than serial on this laptop.

## Slide 9: What the benchmark shows
Chart: 10 million elements (GB/s)
| 1 | 2 | 4 | 8
add | 11.1 | 16.6 | 17.6 | 8.9
mul | 15.7 | 16 | 18.6 | 18.9
Chart: 100,000 elements (speed-up)
| 1 | 2 | 4 | 8
add | 1 | 0.41 | 0.34 | 0.23
mul | 1 | 0.52 | 0.4 | 0.31
Memory bandwidth tops out near 18 GB/s, so extra threads stop helping.
Below 1.0x the threaded run is slower than serial: the cutoff is too low.
Intel Core i7-10510U (4 cores, 8 threads), GCC 16.1, -O3. Single runs on a laptop: expect noise.
Notes: Left: add and mul at 10 million elements are memory-bound; throughput plateaus around 18 GB/s. Right: at 100,000 elements the speed-up is below 1.0, so threads hurt. Numbers come from elementwise_benchmark on the team laptop; they are single runs.

## Slide 10: Takeaways and next steps
3.5–3.8×
dot vs a serial double loop, 1M+ elements
≤ 1.6×
add and mul at 10M elements: bandwidth-bound
0.2–0.5×
add and mul at 100k: slower than serial
Not parallel yet
Packing broadcast and strided inputs
Host copies: from_host, to_vector, to()
Result allocation and validation
Next
Tune the cutoff: sweep 200k to 2M
Parallelise contiguous() and the gather
matmul: cache blocking plus threads
Notes: dot gets about 3.5x because its serial baseline is a double-precision loop. Elementwise ops are limited by memory bandwidth. Next: tune the cutoff from finer sizes, parallelise the strided gather, then matmul, which is compute-bound and should scale best.